## Slide 1
ETH Zürich · Università di Bologna
Mapping-Aware Acceleration of Pointwise (1×1) Convolutions
on the AMD XDNA2 NPU
Project Report
Andrea Massimo Rosetti arosetti@ethz.ch
Supervisor: Prof. Luca Benini
Advisor: <name>
PULP Platform — Open Source Hardware, the way it should be!

## Slide 2
Why pointwise convolutions?
ETH Zürich · Università di Bologna
Andrea Massimo Rosetti 2
NPUs accelerate CNN inference with a grid of many small cores — but they must be fed the right data to stay busy.
1×1 (pointwise) convolutions are everywhere — the expand / project layers of the bottlenecks in ResNet, MobileNet, EfficientNet, ConvNeXt, DenseNet, YOLO…
  They are pure channel mixing (no spatial mixing) → they dominate the channel-wise FLOPs of modern CNNs.
Goal: run them efficiently on the AMD XDNA2 NPU — and understand what actually limits them.

## Slide 3
A 1×1 convolution *is* a matrix multiply
ETH Zürich · Università di Bologna
Andrea Massimo Rosetti 3
For each pixel: output channels = Weights · input channels.
Stack all pixels → a GEMM: M = C_out, K = C_in, N = H·W (pixels), C = A × B.
  Weights→A, activation→B, output→C: the torch NCHW tensors feed the array directly, no transpose.
A = weights [M × K]
×
B = activation [K × N]
=
C = output [M × N]
C_out output channels C_in input channels H·W pixels

## Slide 4
How the GEMM maps onto the NPU array
ETH Zürich · Università di Bologna
Andrea Massimo Rosetti 4
NPU2 (AMD XDNA2, Strix) =
4 rows × 8 columns = 32 cores
Data streams L3 → L2 → L1; cores compute only on L1 tiles.
Columns ↔ pixels (N)
Rows ↔ output channels (M)
K = C_in is the reduction (accumulated over k-blocks).
columns → pixels (8 wide)
rows → C_out (4)

## Slide 5
The problem: column starvation
ETH Zürich · Università di Bologna
Andrea Massimo Rosetti 5
Tall layers have many output channels but few pixels (every 7×7 late layer).
The plain mapping spends the 8-wide column axis on a handful of pixels — mostly zero-padding.
The large C_out dimension — where the work is — gets only 4-way row parallelism.
Across 8 real models: 34% of 1×1 layers are tall, 58% are column-starved (N<512).
only 1 of 8 columns does useful work — the rest is padding

## Slide 6
Contributions
ETH Zürich · Università di Bologna
Andrea Massimo Rosetti 6
Host-side padding (layout-preserving) — any real conv shape runs, no reshaping.
The cols→M axis swap — map C_out onto the 8 columns, where the work is.
  a_col_maj: feed operands as-stored, transpose r×s blocks in the kernel (no illegal DMA transpose).
  Occupancy heuristic — swap only the layers that are actually starved (never a regression).
batch > 1 — per-image dispatch with shared weights.
Full evaluation — 22 shapes from 8 real models, on device, plus a roofline analysis.

## Slide 7
The idea: swap the axes
ETH Zürich · Università di Bologna
Andrea Massimo Rosetti 7
Map columns ↔ C_out (8-wide, where the channels are) and rows ↔ pixels (4-wide, plenty for a few pixels). Put the wide axis where the work is.
Plain: columns ↔ pixels
tall layer → 1/8 columns used
Swap: columns ↔ C_out
8/8 columns filled by channels

## Slide 8
Mechanism: feed as-stored, transpose in the kernel
ETH Zürich · Università di Bologna
Andrea Massimo Rosetti 8
The swap wants the activation as [pixels, C_in], but it is stored [C_in, pixels] — a transpose. A bf16 DMA transpose is illegal (not 4-byte aligned).
Escape: feed each operand as-stored and transpose the small r×s blocks in-register (aie::transpose) — exactly how GEMM already handles b_col_maj / c_col_maj.
array axis
operand (as fed)
flag
rows M̂ = pixels
A = activation [C_in, pixels]
a_col_maj (new)
cols N̂ = C_out
B = weights [C_out, C_in]
b_col_maj
output
C = output [C_out, pixels] (NCHW)
c_col_maj
a_col_maj is the exact mirror of b_col_maj — no host transpose anywhere.

## Slide 9
When does the swap pay off?
ETH Zürich · Università di Bologna
Andrea Massimo Rosetti 9
The in-kernel transpose costs vector cycles — worth it only when the columns are starved.
Auto-heuristic: swap iff ceil(pixels / tile_n) · 2 ≤ columns AND C_out fills more columns.
  i.e. the plain mapping leaves at least half the columns idle.
Wide / already-filled layers auto-decline the swap → never a regression.
  Override with swap_mn = True / False for sweeps.

## Slide 10
Results — the cols→M swap
ETH Zürich · Università di Bologna
Andrea Massimo Rosetti 10
22/22 real-model shapes correct on device. Swap speedup (opt ÷ baseline, cols=8):
6.3×
768/3072/49
4.6×
1024/2048/49
4.4×
512/2048/49
3.3×
2048/512/49
3.2×
3072/768/49
1.8×
384/1536/196
1.3×
112/672/196
C_in / C_out / pixels (7×7 tall layers gain most)
6.3× max 1.8× median

## Slide 11
Results — why the swap exists
ETH Zürich · Università di Bologna
Andrea Massimo Rosetti 11
Throughput vs columns for a tall layer (768/3072/49). Baseline is flat/falling — extra columns are padding. The swap climbs.
211
213
cols=1
206
207
cols=2
187
650
cols=4
165
1074
cols=8
GF/s — gray = plain GEMM, green = swap
165 → 1074 GF/s

## Slide 12
Results — vectorized vs scalar kernel
ETH Zürich · Università di Bologna
Andrea Massimo Rosetti 12
The scalar oracle is pinned at ~6.6 GF/s; the vectorized aie::mmul kernel reaches 575–1042 GF/s.
7
1042
768/3072/49
7
853
384/1536/196
7
641
2048/512/49
8
711
64/256/3136
GF/s — red = scalar, green = vectorized
97× median 156× max

## Slide 13
How close to peak? Occupancy is the limit
ETH Zürich · Università di Bologna
Andrea Massimo Rosetti 13
Same kernel, growing problem: throughput climbs to the ~2.2 TFLOP/s practical peak — but real 1×1 convs are small (N ≤ 196) and can't get there.
8%
N=49
38%
N=196
84%
N=784
91%
N=3136
100%
N=9216
% of empirical peak — real convs live at the left (7–38%)
Latency / occupancy-bound, not bandwidth-bound (eff. BW ≪ peak).
Can't grow the input → recover occupancy structurally with the swap.
  A swapped N=49 layer ≈ a plain N=196 one.

## Slide 14
Putting it together: swap × tile tuning
ETH Zürich · Università di Bologna
Andrea Massimo Rosetti 14
Total speedup over vanilla GEMM = swap × tile tuning (vectorization excluded — scalar is not a real baseline).
6.7×
768/3072/49
4.8×
1024/2048/49
4.8×
512/2048/49
3.8×
2048/512/49
3.2×
3072/768/49
2.2×
384/1536/196
1.7×
1024/512/196
1.7×
112/672/196
bar = total speedup; green = swap, orange = tile tuning
Complementary by design
Swap wins where columns starve (7×7): 3–6× — but there tuning adds little. The swap puts the few pixels on the row axis, pinning m = 16 (49 pixels can't fill a bigger tile without pure padding).
Where pixels are plenty (14×14 / wide), a bigger tile (m = 32–64) is free and amortizes overhead → tuning adds most (up to 1.4×), often on the wide layers the swap declines.
Occupancy (columns) and amortization (tile) — two axes of the same fight.

## Slide 15
Conclusions & future work
ETH Zürich · Università di Bologna
Andrea Massimo Rosetti 15
cols→M swap — put C_out on the 8 columns:
  3–6× on tall layers, 1.8× median, no regressions.
Vectorization — up to 156× over the scalar kernel.
Empirical tile autotuning — up to 1.41×; best tile varies per shape.
Real 1×1 convs are occupancy-bound, not compute-bound — the swap is the right lever.
Future work: single-dispatch batching · int8 · layer fusion
6.3× max swap
156× max vs scalar